## Slide 1
Let's talk about running code efficiently on your local (HPC) system
Robert Jan Schlimbach

## Slide 2: Credit where credit is due
Slides stolen from:
CasparVL
PyTorch
Ezyang
CUDA/cuDNN
  ...and a bit from myself

## Slide 3: The three S'
Know your System
  What kind of hardware do I have?
  What features does my hardware support?
Know your Software
  Does my software do what I want to do efficiently?
  Does my software support my hardware features?
Know your Stack
  What version of software am I running?
  Is my stack compiled for my hardware?

## Slide 4: System
https://servicedesk.surf.nl/wiki/display/WIKI/Snellius+hardware+and+file+systems
Which CPUs?
  X86_64? Aarch64?
What kind of storage?
  SSD (nvme?)? HDD? Tape? Local disk?
What kind of Networking?
  Ethernet? IB?
  IOPs vs Throughput
What kind of RAM?
  HBM? DDR?
  You (AI person) are always memory limited

## Slide 5: System
Goals:
Understand what hardware bottlenecks could be limiting
Understand pro’s and con’s of various hardware
Know how to choose appropriate hardware for you DL task
Know what to do to mitigate bottlenecks

## Slide 6: System
Compute (floating point operations per second, FLOPS)
Memory bandwidth
Memory size
I/O
Communication

## Slide 7: System
Compute (floating point operations per second, FLOPS)
Memory bandwidth
Memory size
I/O
Communication
E.g. training a compute intensive network on a single node

## Slide 8: System
Compute (floating point operations per second, FLOPS)
Memory bandwidth
Memory size
I/O
Communication
Data needs to get to the processor in time in order to do compute!
Many codes are limited by memory bandwidth

## Slide 9: System
Compute (floating point operations per second, FLOPS)
Memory bandwidth
Memory size
I/O
Communication
Very deep or wide networks, or networks with very large input/output layers (e.g. high resolution images) may be limited by memory size.
Not a performance bottleneck, but a no-go!

## Slide 10: System
Compute (floating point operations per second, FLOPS)
Memory bandwidth
Memory size
I/O
Communication
HPC systems typically have shared file systems, usually with good bandwidth, but (relatively) low IOPS
(Very) common bottleneck in distributed learning! Many nodes reading from the same filesystem.
Other users (& sysadmins) will dislike you if you do I/O in a naive way!

## Slide 11: System
Compute (floating point operations per second, FLOPS)
Memory bandwidth
Memory size
I/O
Communication
Communication can be limiting in several ways:
Latency (many, small message send between nodes)
Bandwidth (few, large messages send between nodes)
Load imbalance (some workers in distributed job are slower / have more work; others have to wait when synchronization is needed)
CPU <-> GPU

## Slide 12: System
A look at the hardware, from a DL perspective:
Nvidia is dominant, Volta was a game changer
AMD is finally catching up
Intel Xeon / SPR
AMD Rome
Specialized hardware
I/O
Interconnects
Source: Demystifying Parallel and Distributed Deep Learning: An In-Depth Concurrency Analysis, Ben-Nun & Hoefler 2018

## Slide 13: Hardware overview
Source: Prace best practice guide – deep learning
http://www.prace-ri.eu/IMG/pdf/Best-Practice-Guide-Deep-Learning.pdf
https://en.wikipedia.org/wiki/Ampere_(microarchitecture)
 | INT8 [TOPS] | FP16 [TFLOPS] | Bloat16 | FP32 [TFLOPS] | FP64 [TFLOPS] | Memory [GB] | Memory Bandwidth [GB/s] | PCIe [GB/s] | Proprietary Interconnect [GB/s]
AMD MI60 | 58.9 | 29.5 |  | 14.7 | 7.4 | 32 | 1024 | 31.51 | 200 (2 × 100)
AMD MI100 | 184.6 | 184.6 | 92.3 | 23.1 / 46.1 | 11.5 | 32 | 1200 | 31.51 | 300 (3×100)
AMD MI250 | 362.1 | 362.1 | 362.1 | 45.3 / 90.5 | 45.3 / 90.5 | 128 | 3276.8 | 31.51 | 800 (8 × 100)
NVIDIA V100 | 62.8 | 31.4 / 125 |  | 15.7 | 7.8 | 16/32 | 900 | 15.75 | 300 (6 × 50)
NVIDIA A100 | 624 | 78 / 312 | 312 | 19.5 / 156 | 9.7 / 19.5 | 40/80 | 1555/2039 | 64 | 600
Intel Xeon Scalable 8180 (per socket) | - | - |  | 3.0 / 4.2 | 1.5 / 2.1 | 768 (max) | 119 (max) | 15.75 | -
AMD EPYC 7601 (per socket) | - | - |  | 1.1 / 1.4 | 0.56 / 0.69 | 2000 (max) | 159 (max) | 15.75 | -
Notes: Add H100, add watt en perf per watt, add a10 inference

## Slide 14: Hardware overview
Source: Prace best practice guide – deep learning
http://www.prace-ri.eu/IMG/pdf/Best-Practice-Guide-Deep-Learning.pdf
https://en.wikipedia.org/wiki/Ampere_(microarchitecture)
GPUs support reduced precision, has higher performance
 | INT8 [TOPS] | FP16 [TFLOPS] | Bloat16 | FP32 [TFLOPS] | FP64 [TFLOPS] | Memory [GB] | Memory Bandwidth [GB/s] | PCIe [GB/s] | Proprietary Interconnect [GB/s]
AMD MI60 | 58.9 | 29.5 |  | 14.7 | 7.4 | 32 | 1024 | 31.51 | 200 (2 × 100)
AMD MI100 | 184.6 | 184.6 | 92.3 | 23.1 / 46.1 | 11.5 | 32 | 1200 | 31.51 | 300 (3×100)
AMD MI250 | 362.1 | 362.1 | 362.1 | 45.3 / 90.5 | 45.3 / 90.5 | 128 | 3276.8 | 31.51 | 800 (8 × 100)
NVIDIA V100 | 62.8 | 31.4 / 125 |  | 15.7 | 7.8 | 16/32 | 900 | 15.75 | 300 (6 × 50)
NVIDIA A100 | 624 | 78 / 312 | 312 | 19.5 / 156 | 9.7 / 19.5 | 40/80 | 1555/2039 | 64 | 600
Intel Xeon Scalable 8180 (per socket) | - | - |  | 3.0 / 4.2 | 1.5 / 2.1 | 768 (max) | 119 (max) | 15.75 | -
AMD EPYC 7601 (per socket) | - | - |  | 1.1 / 1.4 | 0.56 / 0.69 | 2000 (max) | 159 (max) | 15.75 | -

## Slide 15: Hardware overview
Source: Prace best practice guide – deep learning
http://www.prace-ri.eu/IMG/pdf/Best-Practice-Guide-Deep-Learning.pdf
https://en.wikipedia.org/wiki/Ampere_(microarchitecture)
GPUs have a lot of FLOPS
compared to CPUs
 | INT8 [TOPS] | FP16 [TFLOPS] | Bloat16 | FP32 [TFLOPS] | FP64 [TFLOPS] | Memory [GB] | Memory Bandwidth [GB/s] | PCIe [GB/s] | Proprietary Interconnect [GB/s]
AMD MI60 | 58.9 | 29.5 |  | 14.7 | 7.4 | 32 | 1024 | 31.51 | 200 (2 × 100)
AMD MI100 | 184.6 | 184.6 | 92.3 | 23.1 / 46.1 | 11.5 | 32 | 1200 | 31.51 | 300 (3×100)
AMD MI250 | 362.1 | 362.1 | 362.1 | 45.3 / 90.5 | 45.3 / 90.5 | 128 | 3276.8 | 31.51 | 800 (8 × 100)
NVIDIA V100 | 62.8 | 31.4 / 125 |  | 15.7 | 7.8 | 16/32 | 900 | 15.75 | 300 (6 × 50)
NVIDIA A100 | 624 | 78 / 312 | 312 | 19.5 / 156 | 9.7 / 19.5 | 40/80 | 1555/2039 | 64 | 600
Intel Xeon Scalable 8180 (per socket) | - | - |  | 3.0 / 4.2 | 1.5 / 2.1 | 768 (max) | 119 (max) | 15.75 | -
AMD EPYC 7601 (per socket) | - | - |  | 1.1 / 1.4 | 0.56 / 0.69 | 2000 (max) | 159 (max) | 15.75 | -

## Slide 16: Hardware overview
Source: Prace best practice guide – deep learning
http://www.prace-ri.eu/IMG/pdf/Best-Practice-Guide-Deep-Learning.pdf
https://en.wikipedia.org/wiki/Ampere_(microarchitecture)
CPUs have a lot of memory compared to GPUs
 | INT8 [TOPS] | FP16 [TFLOPS] | Bloat16 | FP32 [TFLOPS] | FP64 [TFLOPS] | Memory [GB] | Memory Bandwidth [GB/s] | PCIe [GB/s] | Proprietary Interconnect [GB/s]
AMD MI60 | 58.9 | 29.5 |  | 14.7 | 7.4 | 32 | 1024 | 31.51 | 200 (2 × 100)
AMD MI100 | 184.6 | 184.6 | 92.3 | 23.1 / 46.1 | 11.5 | 32 | 1200 | 31.51 | 300 (3×100)
AMD MI250 | 362.1 | 362.1 | 362.1 | 45.3 / 90.5 | 45.3 / 90.5 | 128 | 3276.8 | 31.51 | 800 (8 × 100)
NVIDIA V100 | 62.8 | 31.4 / 125 |  | 15.7 | 7.8 | 16/32 | 900 | 15.75 | 300 (6 × 50)
NVIDIA A100 | 624 | 78 / 312 | 312 | 19.5 / 156 | 9.7 / 19.5 | 40/80 | 1555/2039 | 64 | 600
Intel Xeon Scalable 8180 (per socket) | - | - |  | 3.0 / 4.2 | 1.5 / 2.1 | 768 (max) | 119 (max) | 15.75 | -
AMD EPYC 7601 (per socket) | - | - |  | 1.1 / 1.4 | 0.56 / 0.69 | 2000 (max) | 159 (max) | 15.75 | -

## Slide 17: Hardware overview
 | INT8 [TOPS] | FP16 [TFLOPS] | Bloat16 | FP32 [TFLOPS] | FP64 [TFLOPS] | Memory [GB] | Memory Bandwidth [GB/s] | PCIe [GB/s] | Proprietary Interconnect [GB/s]
AMD MI60 | 58.9 | 29.5 |  | 14.7 | 7.4 | 32 | 1024 | 31.51 | 200 (2 × 100)
AMD MI100 | 184.6 | 184.6 | 92.3 | 23.1 / 46.1 | 11.5 | 32 | 1200 | 31.51 | 300 (3×100)
AMD MI250 | 362.1 | 362.1 | 362.1 | 45.3 / 90.5 | 45.3 / 90.5 | 128 | 3276.8 | 31.51 | 800 (8 × 100)
NVIDIA V100 | 62.8 | 31.4 / 125 |  | 15.7 | 7.8 | 16/32 | 900 | 15.75 | 300 (6 × 50)
NVIDIA A100 | 624 | 78 / 312 | 312 | 19.5 / 156 | 9.7 / 19.5 | 40/80 | 1555/2039 | 64 | 600
Intel Xeon Scalable 8180 (per socket) | - | - |  | 3.0 / 4.2 | 1.5 / 2.1 | 768 (max) | 119 (max) | 15.75 | -
AMD EPYC 7601 (per socket) | - | - |  | 1.1 / 1.4 | 0.56 / 0.69 | 2000 (max) | 159 (max) | 15.75 | -
Source: Prace best practice guide – deep learning
http://www.prace-ri.eu/IMG/pdf/Best-Practice-Guide-Deep-Learning.pdf
https://en.wikipedia.org/wiki/Ampere_(microarchitecture)
Memory bandwidth relative to FLOPS is approximately the same

## Slide 18: Nvidia Volta (e.g. V100, TitanRTX)
Features
INT8 & FP16 support
(Volta) Tensor cores: fused multiply-add units that support mixed precission (multiply in FP16, add in FP32). High performance: 120 TOPS.
High bandwidth memory, 2nd generation (HBM2) (vs. DDR)
Generally you are responsible for specifying a reduced precision: DL frameworks don’t do this automatically since it may impact your networks accuracy, convergence, etc

## Slide 19: Nvidia Ampere GPUs (e.g. A100)
Features (see also https://servicedesk.surf.nl/wiki/display/WIKI/Deep+Learning+on+A100+GPUs )
Tensor Cores support more datatypes (FP64, TF32, FP16, BF16, Int8, Int4, Binary)
TensorFloat32 datatype:
Mixed precision uses FP16. Reduced range causes (potential) need for gradient scaling to prevent underflows

## Slide 20: Nvidia Ampere GPUs (e.g. A100)
Features (see also https://servicedesk.surf.nl/wiki/display/WIKI/Deep+Learning+on+A100+GPUs )
Tensor Cores support more datatypes (FP64, TF32, FP16, BF16, Int8, Int4, Binary)
TensorFloat32 datatype:
TF32 tries to combine best of both worlds: range of an FP32 (no gradient scaling needed), but with reduced precision (for speedup & less memory)

## Slide 21: Nvidia Ampere GPUs (e.g. A100)
Features (see also https://servicedesk.surf.nl/wiki/display/WIKI/Deep+Learning+on+A100+GPUs )
Tensor Cores support more datatypes (FP64, TF32, FP16, BF16, Int8, Int4, Binary)
TensorFloat32 datatype:
Automatically used unless
Environment variable NVIDIA_TF32_OVERRIDE=0 is set
torch.backends.cuda.matmul.allow_tf32 = False and torch.backends.cudnn.allow_tf32 = False are set

## Slide 22: Nvidia Ampere GPUs (e.g. A100)
Model | Precision | Throughput (img/s) | Speedup (compared to FP32) | Loss (1st iteration)
ResNet50 | FP32 | 455.9 | 1 | 7.457645893096924
ResNet50 | TF32 | 750.6 | 1.65 | 7.456507205963135
ResNet50 | FP16 (input) + FP32 (accumulator) | 1087.6 | 2.38 | 7.45703125
VGG19 | FP32 | 212.7 | 1 | 6.9077839851379395
VGG19 | TF32 | 550.3 | 2.59 | 6.907783508300781
VGG19 | FP16 (input) + FP32 (accumulator) | 1099.8 | 5.17 | 6.90625
DenseNet121 | FP32 | 391.9 | 1 | 6.96142053604126
DenseNet121 | TF32 | 591.5 | 1.51 | 6.961450576782227
DenseNet121 | FP16 (input) + FP32 (accumulator) | 876.2 | 2.24 | 6.9609375
Source: https://servicedesk.surf.nl/wiki/display/WIKI/Deep+Learning+on+A100+GPUs

## Slide 23: And on CPU:

## Slide 24: Second S: Software
PyTorch vs Numpy
  PyTorch has GPU support, Numpy does not
  Numpy on AVX2....brrrr
CUDA? ROCm? <insert exotic hardware here>
  E.g.: Intel SapphireRapids
  IPEX: https://github.com/intel/intel-extension-for-pytorch
  LUMI https://www.lumi-supercomputer.eu/
BFloat16 support?

## Slide 25: Third S: Stack
Is my software compiled for my hardware
  Pip install ... ?
  Module load PyTorch/1.12.0-foss-2022a-CUDA-11.7.0
Again: SapphireRapids? ROCm?
PyTorch is crazy: https://github.com/pytorch/pytorch/tree/main/third_party
  PyTorch has given up on generic software management
  Ptrblck:" "

## Slide 26: Wait ... so what happens?
You call torch
  (Manual) Dispatching
  E.g. scatter_add_ -> Message psasing in Graph-NNs
Torch (python) determines the most appropriate function to call
  Dispatching
Torch (C++/CU) calls the CPU/GPU kernel
  Dispatching
Low-level lib performs actual calculation
  Dispatching
PyTorch Dispatcher: http://blog.ezyang.com/2020/09/lets-talk-about-the-pytorch-dispatcher/
Your choices matter

## Slide 27: In practice: PyTorch + Snellius
We only have A100 GPUs (H100's coming?)
  https://servicedesk.surf.nl/wiki/display/WIKI/Deep+Learning+on+A100+GPUs
Makes optimization a bit easier for you
You only need to spend a year sifting through documentation
  Or ask us... :)
  Every EINF has a default of 4 consultancy hours

## Slide 28: Rapidfire: implementation details
How fast do you want to go?
https://pytorch.org/docs/stable/notes/cuda.html
https://docs.nvidia.com/deeplearning/performance/dl-performance-memory-limited/index.html
https://docs.nvidia.com/deeplearning/performance/index.html
Duncan: "You can take any piece of code, spend 6 months optimizing it, and then write a paper about it"

## Slide 29: Rapidfire: implementation details
How fast do you want to go?
What is your goal?
  Largest model possible?
  Best validation performance?
  Submit a paper to ISC '23?

## Slide 30: Rapidfire: implementation details

## Slide 31: Level 1: shouldn't impact model convergence:

## Slide 32: Level 1: shouldn't impact model convergence:
Avoid CPU-GPU sync
  Create tensors directly on the device
Don't (accidentally) aggregate tensors which still require grad, e.g.: losses.append(loss) (:o)

## Slide 33: Level 1: shouldn't impact model convergence:
torch.backends.cuda.matmul.allow_tf32 = True
  The default in PyTorch (silently)
torch.set_float32_matmul_precision('high')
torch.backends.cudnn.benchmark = True
Align bytes: multiples of 2, 8, 1024
  DNN libs want nicely aligned memory
torch.channels_last
JIT/Compile: PyTorch 2.0

## Slide 34: Level 2: Danger zone
torch.backends.cuda.matmul.allow_fp16_reduced_precision_reduction = True
torch.backends.cuda.matmul.allow_bf16_reduced_precision_reduction = True
Lol:
Torch.set_float32_matmul_precision('medium')
Cast model and data to (B)Float16 before the forward pass
  We're not supposed to...but:

## Slide 35: Change your model
  Worst case scenario:

## Slide 37: Always
  Have a baseline
  Check convergence statistics

## Slide 38: Profile
  Profile
  Profile
  Profile

## Slide 39: More generally; listen to Duncan:
  Start small
  Have a goal
  Profile your code