## Slide 1
Make Snellius go fast(er)
Robert Jan Schlimbach & Lars Veefkind
Team High-Performance Machine-Learning

## Slide 2: Who am I & What does SURF do
Me:
UvA AI grad
HPC ML advisor at SURF
Love making code go fast
Love running, climbing, and mountains
SURF
Help academia in a very broad sense
Eduroam, SurfConext, SurfMarket, National Supercomputer, etc...

## Slide 3: The program
Quick intro to Snellius and the three S' (20 minutes)
The big fat list of ML optimization on Snellius (10 minutes)
Profiling PyTorch (60 minutes)

## Slide 4: What is a supercomputer/clustercomputer
Practically: a bunch of (very big) computers tied together
Uses hardware/software which is not available for regular consumers
Very fast Interconnect
  Ethernet/IB/GPU-direct
Very fast Storage
  Tiered: NVME/Hard-disk/Tape
Very fast Compute
  Accelerators
  Huge CPUs
  Massive amounts of RAM

## Slide 5: Snellius
~1300 CPU-based nodes
  128-192 cores
  256-378 GB RAM
~100 high-memory nodes
  1TB-8TB RAM
160 GPU nodes
  x4 nvidia A100s / H100s
  512GB RAM
  40GB /94 GB VRAM
Storage:
  ~13PB of medium-speed storage project space
  720TB of home-dir
  210TB of NVME
Interconnect: 100GBps Infiniband fat-tree

## Slide 6: The three S'
Know your System
  What kind of hardware do I have?
  What features does my hardware support?
Know your Software
  Does my software do what I want to do efficiently?
  Does my software support my hardware features?
Know your Stack
  What version of software am I running?
  Is my stack compiled for my hardware?

## Slide 7: System
Which CPUs?
  Architectures: X86_64, ARM64
What kind of storage?
  SSD, HDD, Tape?
  SATA, NVMe or full PCI-E?
What kind of Networking?
  Ethernet? InfiniBand (IB)?
  IOPs vs Throughput
What kind of RAM?
  High Bandwidth Memory (HBM) or Data Double Rate (DDR)?
  How much? Enough for a RAMdisk?
  You (AI person) are always memory limited
Which GPUs?
  AMD? Good raw performance, poor PyTorch support (for now)
  NVIDIA? Optimized for AI with good PyTorch support.
https://servicedesk.surf.nl/wiki/display/WIKI/Snellius+hardware+and+file+systems

## Slide 8: System
Goals:
Understand what hardware bottlenecks could be limitting
Understand pro’s and con’s of various hardware
Know how to choose appropriate hardware for you DL task
Know what to do to mitigate bottlenecks

## Slide 9: System
Compute (floating point operations per second, FLOPS)
Memory bandwidth
Memory size
I/O
Communication

## Slide 10: System
Compute (floating point operations per second, FLOPS)
Memory bandwidth
Memory size
I/O
Communication
E.g. training a compute intensive network on a single node

## Slide 11: System
Compute (floating point operations per second, FLOPS)
Memory bandwidth
Memory size
I/O
Communication
Data needs to get to the processor in time in order to do compute!
Many codes are limited by memory bandwidth

## Slide 12: System
Compute (floating point operations per second, FLOPS)
Memory bandwidth
Memory size
I/O
Communication
Very deep or wide networks, or networks with very large input/output layers (e.g. high resolution images) may be limited by memory size.
Not a performance bottleneck, but a no-go!

## Slide 13: System
Compute (floating point operations per second, FLOPS)
Memory bandwidth
Memory size
I/O
Communication
HPC systems typically have shared file systems, usually with good bandwidth, but (relatively) low I/O operations per second (IOPS)
Common bottleneck in distributed learning! Many nodes reading from the same filesystem.
Other users (& sysadmins) will dislike you if you do I/O in a naive way!

## Slide 14: System
Compute (floating point operations per second, FLOPS)
Memory bandwidth
Memory size
I/O
Communication
Communication can be limiting in several ways:
Latency (many, small message send between nodes)
Bandwidth (few, large messages send between nodes)
Load imbalance (some workers in distributed job are slower / have more work; others have to wait when synchronization is needed)
CPU <-> GPU

## Slide 15: System
A look at the hardware, from a DL perspective:
Nvidia is dominant, Volta was a game changer
AMD is finally catching up
Specialized hardware losing favour
Same for CPUs
Source: Demystifying Parallel and Distributed Deep Learning: An In-Depth Concurrency Analysis, Ben-Nun & Hoefler 2018

## Slide 16: Hardware overview
 | FP8 [TFLOPS] | INT8 [TOPS] | FP16 [TFLOPS] | Bloat16 [TFLOPS] | FP32 [TFLOPS] | FP64 [TFLOPS] | Memory [GB] | Memory Bandwidth [GB/s] | PCIe [GB/s] | Power draw [W] | FP16 TFLOP per Watt
AMD MI250 |  | 362.1 | 362.1 | 362.1 | 90.5 | 90.5 | 128 | 3276.8 | 31.51 | 560 | 0.64
AMD MI300x |  | 2615 | 1307 | 1307 | 654 | 163 | 192 | 5300 | 128 | 750 | 1.74
NVIDIA A100 |  | 624 | 312 | 312 | 156 | 19.5 | 40/80 | 1555-2039 | 64 | 400 | 0.78
NVIDIA H100 | 1979 | 1979 | 990 | 990 | 989 | 67 | 80/96 | 2000-3900 | 128 | 700 | 1.32
NVIDIA L40S (inference only) | 733 | 733 | 362 | 362 | 183 | 1.4 | 48 | 864 | 64 | 350 | 1.03
NVIDIA RTX 4090 (consumer) | 330 | 660 | 165 | 165 | 83 | 1.2 | 24 | 1000 | 64 | 400 | 0.41
Intel Xeon Scalable 8180 (per socket) |  | - | - |  | 4.2 | 2.1 | 768 (max) | 119 (max) | 15.75 | 205 | 0.02
AMD EPYC 7601 (per socket) |  | - | - |  | 1.4 | 0.69 | 2000 (max) | 159 (max) | 15.75 | 180 | 0.008
Prace best practice guide – deep learning
https://en.wikipedia.org/wiki/Ampere_(microarchitecture)
Notes: Add H100, add watt en perf per watt, add a10 inference

## Slide 17: Hardware overview
 | FP8 [TFLOPS] | INT8 [TOPS] | FP16 [TFLOPS] | Bloat16 [TFLOPS] | FP32 [TFLOPS] | FP64 [TFLOPS] | Memory [GB] | Memory Bandwidth [GB/s] | PCIe [GB/s] | Power draw [W] | FP16 TFLOP per Watt
AMD MI250 |  | 362.1 | 362.1 | 362.1 | 90.5 | 90.5 | 128 | 3276.8 | 31.51 | 560 | 0.64
AMD MI300x |  | 2615 | 1307 | 1307 | 654 | 163 | 192 | 5300 | 128 | 750 | 1.74
NVIDIA A100 |  | 624 | 312 | 312 | 156 | 19.5 | 40/80 | 1555-2039 | 64 | 400 | 0.78
NVIDIA H100 | 1979 | 1979 | 990 | 990 | 989 | 67 | 80/96 | 2000-3900 | 128 | 700 | 1.32
NVIDIA L40S (inference only) | 733 | 733 | 362 | 362 | 183 | 1.4 | 48 | 864 | 64 | 350 | 1.03
NVIDIA RTX 4090 (consumer) | 330 | 660 | 165 | 165 | 83 | 1.2 | 24 | 1000 | 64 | 400 | 0.41
Intel Xeon Scalable 8180 (per socket) |  | - | - |  | 4.2 | 2.1 | 768 (max) | 119 (max) | 15.75 | 205 | 0.02
AMD EPYC 7601 (per socket) |  | - | - |  | 1.4 | 0.69 | 2000 (max) | 159 (max) | 15.75 | 180 | 0.008
Prace best practice guide – deep learning
https://en.wikipedia.org/wiki/Ampere_(microarchitecture)
GPUs support reduced precision, has higher performance
Notes: Add H100, add watt en perf per watt, add a10 inference

## Slide 18: Hardware overview
 | FP8 [TFLOPS] | INT8 [TOPS] | FP16 [TFLOPS] | Bloat16 [TFLOPS] | FP32 [TFLOPS] | FP64 [TFLOPS] | Memory [GB] | Memory Bandwidth [GB/s] | PCIe [GB/s] | Power draw [W] | FP16 TFLOP per Watt
AMD MI250 |  | 362.1 | 362.1 | 362.1 | 90.5 | 90.5 | 128 | 3276.8 | 31.51 | 560 | 0.64
AMD MI300x |  | 2615 | 1307 | 1307 | 654 | 163 | 192 | 5300 | 128 | 750 | 1.74
NVIDIA A100 |  | 624 | 312 | 312 | 156 | 19.5 | 40/80 | 1555-2039 | 64 | 400 | 0.78
NVIDIA H100 | 1979 | 1979 | 990 | 990 | 989 | 67 | 80/96 | 2000-3900 | 128 | 700 | 1.32
NVIDIA L40S (inference only) | 733 | 733 | 362 | 362 | 183 | 1.4 | 48 | 864 | 64 | 350 | 1.03
NVIDIA RTX 4090 (consumer) | 330 | 660 | 165 | 165 | 83 | 1.2 | 24 | 1000 | 64 | 400 | 0.41
Intel Xeon Scalable 8180 (per socket) |  | - | - |  | 4.2 | 2.1 | 768 (max) | 119 (max) | 15.75 | 205 | 0.02
AMD EPYC 7601 (per socket) |  | - | - |  | 1.4 | 0.69 | 2000 (max) | 159 (max) | 15.75 | 180 | 0.008
Prace best practice guide – deep learning
https://en.wikipedia.org/wiki/Ampere_(microarchitecture)
GPUs have a lot of FLOPS
compared to CPUs
Notes: Add H100, add watt en perf per watt, add a10 inference

## Slide 19: Hardware overview
 | FP8 [TFLOPS] | INT8 [TOPS] | FP16 [TFLOPS] | Bloat16 [TFLOPS] | FP32 [TFLOPS] | FP64 [TFLOPS] | Memory [GB] | Memory Bandwidth [GB/s] | PCIe [GB/s] | Power draw [W] | FP16 TFLOP per Watt
AMD MI250 |  | 362.1 | 362.1 | 362.1 | 90.5 | 90.5 | 128 | 3276.8 | 31.51 | 560 | 0.64
AMD MI300x |  | 2615 | 1307 | 1307 | 654 | 163 | 192 | 5300 | 128 | 750 | 1.74
NVIDIA A100 |  | 624 | 312 | 312 | 156 | 19.5 | 40/80 | 1555-2039 | 64 | 400 | 0.78
NVIDIA H100 | 1979 | 1979 | 990 | 990 | 989 | 67 | 80/96 | 2000-3900 | 128 | 700 | 1.32
NVIDIA L40S (inference only) | 733 | 733 | 362 | 362 | 183 | 1.4 | 48 | 864 | 64 | 350 | 1.03
NVIDIA RTX 4090 (consumer) | 330 | 660 | 165 | 165 | 83 | 1.2 | 24 | 1000 | 64 | 400 | 0.41
Intel Xeon Scalable 8180 (per socket) |  | - | - |  | 4.2 | 2.1 | 768 (max) | 119 (max) | 15.75 | 205 | 0.02
AMD EPYC 7601 (per socket) |  | - | - |  | 1.4 | 0.69 | 2000 (max) | 159 (max) | 15.75 | 180 | 0.008
Prace best practice guide – deep learning
https://en.wikipedia.org/wiki/Ampere_(microarchitecture)
CPUs have a lot of memory compared to GPUs
Notes: Add H100, add watt en perf per watt, add a10 inference

## Slide 20: Hardware overview
 | FP8 [TFLOPS] | INT8 [TOPS] | FP16 [TFLOPS] | Bloat16 [TFLOPS] | FP32 [TFLOPS] | FP64 [TFLOPS] | Memory [GB] | Memory Bandwidth [GB/s] | PCIe [GB/s] | Power draw [W] | FP16 TFLOP per Watt
AMD MI250 |  | 362.1 | 362.1 | 362.1 | 90.5 | 90.5 | 128 | 3276.8 | 31.51 | 560 | 0.64
AMD MI300x |  | 2615 | 1307 | 1307 | 654 | 163 | 192 | 5300 | 128 | 750 | 1.74
NVIDIA A100 |  | 624 | 312 | 312 | 156 | 19.5 | 40/80 | 1555-2039 | 64 | 400 | 0.78
NVIDIA H100 | 1979 | 1979 | 990 | 990 | 989 | 67 | 80/96 | 2000-3900 | 128 | 700 | 1.32
NVIDIA L40S (inference only) | 733 | 733 | 362 | 362 | 183 | 1.4 | 48 | 864 | 64 | 350 | 1.03
NVIDIA RTX 4090 (consumer) | 330 | 660 | 165 | 165 | 83 | 1.2 | 24 | 1000 | 64 | 400 | 0.41
Intel Xeon Scalable 8180 (per socket) |  | - | - |  | 4.2 | 2.1 | 768 (max) | 119 (max) | 15.75 | 205 | 0.02
AMD EPYC 7601 (per socket) |  | - | - |  | 1.4 | 0.69 | 2000 (max) | 159 (max) | 15.75 | 180 | 0.008
Prace best practice guide – deep learning
https://en.wikipedia.org/wiki/Ampere_(microarchitecture)
Memory bandwidth relative to FLOPS is approximately the same
Notes: Add H100, add watt en perf per watt, add a10 inference

## Slide 21: Hardware overview
 | FP8 [TFLOPS] | INT8 [TOPS] | FP16 [TFLOPS] | Bloat16 [TFLOPS] | FP32 [TFLOPS] | FP64 [TFLOPS] | Memory [GB] | Memory Bandwidth [GB/s] | PCIe [GB/s] | Power draw [W] | FP16 TFLOP per Watt
AMD MI250 |  | 362.1 | 362.1 | 362.1 | 90.5 | 90.5 | 128 | 3276.8 | 31.51 | 560 | 0.64
AMD MI300x |  | 2615 | 1307 | 1307 | 654 | 163 | 192 | 5300 | 128 | 750 | 1.74
NVIDIA A100 |  | 624 | 312 | 312 | 156 | 19.5 | 40/80 | 1555-2039 | 64 | 400 | 0.78
NVIDIA H100 | 1979 | 1979 | 990 | 990 | 989 | 67 | 80/96 | 2000-3900 | 128 | 700 | 1.32
NVIDIA L40S (inference only) | 733 | 733 | 362 | 362 | 183 | 1.4 | 48 | 864 | 64 | 350 | 1.03
NVIDIA RTX 4090 (consumer) | 330 | 660 | 165 | 165 | 83 | 1.2 | 24 | 1000 | 64 | 400 | 0.41
Intel Xeon Scalable 8180 (per socket) |  | - | - |  | 4.2 | 2.1 | 768 (max) | 119 (max) | 15.75 | 205 | 0.02
AMD EPYC 7601 (per socket) |  | - | - |  | 1.4 | 0.69 | 2000 (max) | 159 (max) | 15.75 | 180 | 0.008
Prace best practice guide – deep learning
https://en.wikipedia.org/wiki/Ampere_(microarchitecture)
GPU price is often irrelevant, but the performance per Watt is.
Notes: Add H100, add watt en perf per watt, add a10 inference

## Slide 22: Nvidia Volta (e.g. V100, TitanRTX)
Features
INT8 & FP16 support
(Volta) Tensor cores: fused multiply-add units that support mixed precision (multiply in FP16, add in FP32). High performance: 120 TFLOPS (for the time).
High bandwidth memory, 2nd generation (HBM2) (vs. DDR)
Generally, you are responsible for specifying a reduced precision: DL frameworks don’t do this automatically since it may impact your networks accuracy, convergence, etc

## Slide 23: Nvidia Ampere GPUs (e.g. A100)
Features (see also https://servicedesk.surf.nl/wiki/display/WIKI/Deep+Learning+on+A100+GPUs )
Tensor Cores support more datatypes (FP64, TF32, FP16, BF16, Int8, Int4, Binary)
TensorFloat32 datatype:
Mixed precision uses FP16. Reduced range causes (potential) need for gradient scaling to prevent underflows

## Slide 24: Nvidia Ampere GPUs (e.g. A100)
Features (see also https://servicedesk.surf.nl/wiki/display/WIKI/Deep+Learning+on+A100+GPUs )
Tensor Cores support more datatypes (FP64, TF32, FP16, BF16, Int8, Int4, Binary)
TensorFloat32 datatype:
TF32 tries to combine best of both worlds: range of an FP32 (no gradient scaling needed), but with reduced precision (for speedup & less memory)

## Slide 25: Nvidia Ampere GPUs (e.g. A100)
Features (see also https://servicedesk.surf.nl/wiki/display/WIKI/Deep+Learning+on+A100+GPUs )
Tensor Cores support more datatypes (FP64, TF32, FP16, BF16, Int8, Int4, Binary)
TensorFloat32 datatype:
Automatically used unless
Environment variable NVIDIA_TF32_OVERRIDE=0 is set
torch.backends.cuda.matmul.allow_tf32 = False and torch.backends.cudnn.allow_tf32 = False are set

## Slide 26: Nvidia Ampere GPUs (e.g. A100)
Model | Precision | Throughput (img/s) | Speedup (compared to FP32) | Loss (1st iteration)
ResNet50 | FP32 | 455.9 | 1 | 7.457645893096924
ResNet50 | TF32 | 750.6 | 1.65 | 7.456507205963135
ResNet50 | FP16 (input) + FP32 (accumulator) | 1087.6 | 2.38 | 7.45703125
VGG19 | FP32 | 212.7 | 1 | 6.9077839851379395
VGG19 | TF32 | 550.3 | 2.59 | 6.907783508300781
VGG19 | FP16 (input) + FP32 (accumulator) | 1099.8 | 5.17 | 6.90625
DenseNet121 | FP32 | 391.9 | 1 | 6.96142053604126
DenseNet121 | TF32 | 591.5 | 1.51 | 6.961450576782227
DenseNet121 | FP16 (input) + FP32 (accumulator) | 876.2 | 2.24 | 6.9609375
Source: https://servicedesk.surf.nl/wiki/display/WIKI/Deep+Learning+on+A100+GPUs

## Slide 27: Nvidia Hopper GPUs (e.g. H100)
FP8 support
Transformer-specific optimizations

## Slide 28: And on CPU:
Notes: Add new cpus

## Slide 29: Second S: Software
PyTorch/TensorFlow vs Numpy
  PyTorch and TensorFlow have GPU support, Numpy does not
  Numpy on AVX2....brrrr
Support for CUDA (Nvidia), ROCm (AMD), <insert exotic hardware here>?
  E.g.: Intel SapphireRapids
  IPEX: https://github.com/intel/intel-extension-for-pytorch
  LUMI https://www.lumi-supercomputer.eu/
Support for lower precision
  BFloat16, Float16?

## Slide 30: Third S: Stack
Is my software compiled for my hardware
  Pip install … ?
  Module load PyTorch/2.1.2-foss-2023a-CUDA-12.1.1
Again: SapphireRapids? ROCm?
PyTorch is crazy: https://github.com/pytorch/pytorch/tree/main/third_party
  PyTorch has given up on generic software management
  Ptrblck: " (but for PyTorch most of the time it doesn't matter (if you're doing the usual stuff))

## Slide 31: Wait ... so what happens?
You call torch
  (Manual) Dispatching
  E.g. scatter_add_ -> Message passing in Graph-NNs
Torch (python) determines the most appropriate function to call
  Dispatching
Torch (C++/CU) calls the CPU/GPU kernel
  Dispatching
Low-level lib performs actual calculation
  Dispatching
PyTorch Dispatcher: http://blog.ezyang.com/2020/09/lets-talk-about-the-pytorch-dispatcher/
Your choices matter

## Slide 32: In practice: PyTorch + Snellius
We only have NVIDIA GPUs
  72x4=288 NVIDIA A100
  88x4=352 NVIDIA H100 (added recently)
Makes optimization a bit easier for you
You only need to spend a year sifting through documentation
  https://servicedesk.surf.nl/wiki/display/WIKI/Deep+Learning+on+A100+GPUs
  Or ask us... :)
  Every EINF/NWO small grants has a default of 4 consultancy hours

## Slide 33: Rapidfire: implementation details
How fast do you want to go?
What is your goal?
  Largest model possible?
  Best validation performance?
  Submit a paper to ISC '25?

## Slide 34: Rapidfire: implementation details
How fast do you want to go?
https://pytorch.org/docs/stable/notes/cuda.html
https://docs.nvidia.com/deeplearning/performance/dl-performance-memory-limited/index.html
https://docs.nvidia.com/deeplearning/performance/index.html
Duncan: "You can take any piece of code, spend 6 months optimizing it, and then write a paper about it"

## Slide 35: First of all and last of all: monitoring & profiling
You don't know if you don't know
Monitoring:
  Wandb
  CPU: Top / htop
  GPU: nvidia-smi / nvtop / dcgmi
Profiling
  Torch-tb-profiler / Hollistic Trace Analysis
  Nsight systems
  Nsight compute

## Slide 36: Rapidfire: implementation details

## Slide 37: Level 0: We will reject your grant request if you don't do this (and don't have a good reason not to do so)
Torch.compile
Using lower precision, e.g. BFloat16

## Slide 38: Level 1: Doesn't impact model performance; 'tricks'

## Slide 39: Level 1: Doesn't impact model performance
Avoid CPU-GPU sync
  Create tensors directly on the device
Don't aggregate tensors which still require grad, e.g.: losses.append(loss) (:o)
  instead, detach (loss.detach())

## Slide 40: Level 1: Doesn't impact model performance; 'tricks'
torch.backends.cuda.matmul.allow_tf32 = True
  The default in PyTorch (silently)
torch.set_float32_matmul_precision('high')
torch.backends.cudnn.benchmark = True
  Empirically benchmarks to find fastest method
Align bytes: multiples of 2, 8, 1024
  DNN libraries want nicely aligned memory
torch.channels_last
  Helps with memory alignment and reduces cache misses
Reinforcement learning specific:
  Use Nvidia MPS (basically a scheduler for GPUs)

## Slide 41: Level 2: Danger zone
Quantization is becoming more and more important
  Huggingface makes it easy for you, e.g. LLM.int8
  PyTorch is finally catching up: https://pytorch.org/blog/pytorch-native-architecture-optimization/

## Slide 42: Level 2: Danger zone
torch.backends.cuda.matmul.allow_fp16_reduced_precision_reduction = True
Lol:
torch.backends.cuda.matmul.allow_bf16_reduced_precision_reduction
Torch.set_float32_matmul_precision('medium')
Cast model and data to (B)Float16 before the forward pass
  We're not supposed to...but:

## Slide 43: Change your model
  Worst case scenario:

## Slide 45: Always
  Have a baseline
  Check convergence statistics

## Slide 46: Profile
  Get a grip on your model’s performance
  Profile
  Profile
  Profile
  Also important: profile

## Slide 47: More generally; listen to Duncan:
  Start small
  Have a goal
  Profile your code