## Slide 1
Hardware and software features to accelerate deep learning

## Slide 2: The three S'
Know your System
  What kind of hardware do I have?
  What features does my hardware support?
Know your Software
  Does my software do what I want to do efficiently?
  Does my software support my hardware features?
Know your Stack
  What version of software am I running?
  Is my stack compiled for my hardware?

## Slide 3: System
Which CPUs?
  Architectures: X86_64, ARM64
What kind of storage?
  SSD, HDD, Tape?
  SATA, NVMe or full PCI-E?
What kind of Networking?
  Ethernet? InfiniBand (IB)?
  IOPs vs Throughput
What kind of RAM?
  High Bandwidth Memory (HBM) or Data Double Rate (DDR)?
  How much? Enough for a RAMdisk?
  You (AI person) are always memory limited
Which GPUs?
  AMD? Good raw performance, poor PyTorch support (for now)
  NVIDIA? Optimized for AI with good PyTorch support.
https://servicedesk.surf.nl/wiki/display/WIKI/Snellius+hardware+and+file+systems

## Slide 4: System
Goals:
Understand what hardware bottlenecks could be limitting
Understand pro’s and con’s of various hardware
Know how to choose appropriate hardware for you DL task
Know what to do to mitigate bottlenecks

## Slide 5: System
Compute (floating point operations per second, FLOPS)
Memory bandwidth
Memory size
I/O
Communication

## Slide 6: System
Compute (floating point operations per second, FLOPS)
Memory bandwidth
Memory size
I/O
Communication
E.g. training a compute intensive network on a single node

## Slide 7: System
Compute (floating point operations per second, FLOPS)
Memory bandwidth
Memory size
I/O
Communication
Data needs to get to the processor in time in order to do compute!
Many codes are limited by memory bandwidth

## Slide 8: System
Compute (floating point operations per second, FLOPS)
Memory bandwidth
Memory size
I/O
Communication
Very deep or wide networks, or networks with very large input/output layers (e.g. high resolution images) may be limited by memory size.
Not a performance bottleneck, but a no-go!

## Slide 9: System
Compute (floating point operations per second, FLOPS)
Memory bandwidth
Memory size
I/O
Communication
HPC systems typically have shared file systems, usually with good bandwidth, but (relatively) low I/O operations per second (IOPS)
Common bottleneck in distributed learning! Many nodes reading from the same filesystem.
Other users (& sysadmins) will dislike you if you do I/O in a naive way!

## Slide 10: System
Compute (floating point operations per second, FLOPS)
Memory bandwidth
Memory size
I/O
Communication
Communication can be limiting in several ways:
Latency (many, small message send between nodes)
Bandwidth (few, large messages send between nodes)
Load imbalance (some workers in distributed job are slower / have more work; others have to wait when synchronization is needed)
CPU <-> GPU

## Slide 11: System
A look at the hardware, from a DL perspective:
Nvidia is dominant, Volta was a game changer
AMD is finally catching up
Specialized hardware losing favour
Same for CPUs
Source: Demystifying Parallel and Distributed Deep Learning: An In-Depth Concurrency Analysis, Ben-Nun & Hoefler 2018

## Slide 12: Hardware overview
 | FP8 [TFLOPS] | INT8 [TOPS] | FP16 [TFLOPS] | Bloat16 [TFLOPS] | FP32 [TFLOPS] | FP64 [TFLOPS] | Memory [GB] | Memory Bandwidth [GB/s] | PCIe [GB/s] | Power draw [W] | FP16 TFLOP per Watt
AMD MI250 |  | 362.1 | 362.1 | 362.1 | 90.5 | 90.5 | 128 | 3276.8 | 31.51 | 560 | 0.64
AMD MI300x |  | 2615 | 1307 | 1307 | 654 | 163 | 192 | 5300 | 128 | 750 | 1.74
NVIDIA A100 |  | 624 | 312 | 312 | 156 | 19.5 | 40/80 | 1555-2039 | 64 | 400 | 0.78
NVIDIA H100 | 1979 | 1979 | 990 | 990 | 989 | 67 | 80/96 | 2000-3900 | 128 | 700 | 1.32
NVIDIA L40S (inference only) | 733 | 733 | 362 | 362 | 183 | 1.4 | 48 | 864 | 64 | 350 | 1.03
NVIDIA RTX 4090 (consumer) | 330 | 660 | 165 | 165 | 83 | 1.2 | 24 | 1000 | 64 | 400 | 0.41
Intel Xeon Scalable 8180 (per socket) |  | - | - |  | 4.2 | 2.1 | 768 (max) | 119 (max) | 15.75 | 205 | 0.02
AMD EPYC 7601 (per socket) |  | - | - |  | 1.4 | 0.69 | 2000 (max) | 159 (max) | 15.75 | 180 | 0.008
Prace best practice guide – deep learning
https://en.wikipedia.org/wiki/Ampere_(microarchitecture)
Notes: Add H100, add watt en perf per watt, add a10 inference

## Slide 13: Hardware overview
 | FP8 [TFLOPS] | INT8 [TOPS] | FP16 [TFLOPS] | Bloat16 [TFLOPS] | FP32 [TFLOPS] | FP64 [TFLOPS] | Memory [GB] | Memory Bandwidth [GB/s] | PCIe [GB/s] | Power draw [W] | FP16 TFLOP per Watt
AMD MI250 |  | 362.1 | 362.1 | 362.1 | 90.5 | 90.5 | 128 | 3276.8 | 31.51 | 560 | 0.64
AMD MI300x |  | 2615 | 1307 | 1307 | 654 | 163 | 192 | 5300 | 128 | 750 | 1.74
NVIDIA A100 |  | 624 | 312 | 312 | 156 | 19.5 | 40/80 | 1555-2039 | 64 | 400 | 0.78
NVIDIA H100 | 1979 | 1979 | 990 | 990 | 989 | 67 | 80/96 | 2000-3900 | 128 | 700 | 1.32
NVIDIA L40S (inference only) | 733 | 733 | 362 | 362 | 183 | 1.4 | 48 | 864 | 64 | 350 | 1.03
NVIDIA RTX 4090 (consumer) | 330 | 660 | 165 | 165 | 83 | 1.2 | 24 | 1000 | 64 | 400 | 0.41
Intel Xeon Scalable 8180 (per socket) |  | - | - |  | 4.2 | 2.1 | 768 (max) | 119 (max) | 15.75 | 205 | 0.02
AMD EPYC 7601 (per socket) |  | - | - |  | 1.4 | 0.69 | 2000 (max) | 159 (max) | 15.75 | 180 | 0.008
Prace best practice guide – deep learning
https://en.wikipedia.org/wiki/Ampere_(microarchitecture)
GPUs support reduced precision, has higher performance
Notes: Add H100, add watt en perf per watt, add a10 inference

## Slide 14: Hardware overview
 | FP8 [TFLOPS] | INT8 [TOPS] | FP16 [TFLOPS] | Bloat16 [TFLOPS] | FP32 [TFLOPS] | FP64 [TFLOPS] | Memory [GB] | Memory Bandwidth [GB/s] | PCIe [GB/s] | Power draw [W] | FP16 TFLOP per Watt
AMD MI250 |  | 362.1 | 362.1 | 362.1 | 90.5 | 90.5 | 128 | 3276.8 | 31.51 | 560 | 0.64
AMD MI300x |  | 2615 | 1307 | 1307 | 654 | 163 | 192 | 5300 | 128 | 750 | 1.74
NVIDIA A100 |  | 624 | 312 | 312 | 156 | 19.5 | 40/80 | 1555-2039 | 64 | 400 | 0.78
NVIDIA H100 | 1979 | 1979 | 990 | 990 | 989 | 67 | 80/96 | 2000-3900 | 128 | 700 | 1.32
NVIDIA L40S (inference only) | 733 | 733 | 362 | 362 | 183 | 1.4 | 48 | 864 | 64 | 350 | 1.03
NVIDIA RTX 4090 (consumer) | 330 | 660 | 165 | 165 | 83 | 1.2 | 24 | 1000 | 64 | 400 | 0.41
Intel Xeon Scalable 8180 (per socket) |  | - | - |  | 4.2 | 2.1 | 768 (max) | 119 (max) | 15.75 | 205 | 0.02
AMD EPYC 7601 (per socket) |  | - | - |  | 1.4 | 0.69 | 2000 (max) | 159 (max) | 15.75 | 180 | 0.008
Prace best practice guide – deep learning
https://en.wikipedia.org/wiki/Ampere_(microarchitecture)
GPUs have a lot of FLOPS
compared to CPUs
Notes: Add H100, add watt en perf per watt, add a10 inference

## Slide 15: Hardware overview
 | FP8 [TFLOPS] | INT8 [TOPS] | FP16 [TFLOPS] | Bloat16 [TFLOPS] | FP32 [TFLOPS] | FP64 [TFLOPS] | Memory [GB] | Memory Bandwidth [GB/s] | PCIe [GB/s] | Power draw [W] | FP16 TFLOP per Watt
AMD MI250 |  | 362.1 | 362.1 | 362.1 | 90.5 | 90.5 | 128 | 3276.8 | 31.51 | 560 | 0.64
AMD MI300x |  | 2615 | 1307 | 1307 | 654 | 163 | 192 | 5300 | 128 | 750 | 1.74
NVIDIA A100 |  | 624 | 312 | 312 | 156 | 19.5 | 40/80 | 1555-2039 | 64 | 400 | 0.78
NVIDIA H100 | 1979 | 1979 | 990 | 990 | 989 | 67 | 80/96 | 2000-3900 | 128 | 700 | 1.32
NVIDIA L40S (inference only) | 733 | 733 | 362 | 362 | 183 | 1.4 | 48 | 864 | 64 | 350 | 1.03
NVIDIA RTX 4090 (consumer) | 330 | 660 | 165 | 165 | 83 | 1.2 | 24 | 1000 | 64 | 400 | 0.41
Intel Xeon Scalable 8180 (per socket) |  | - | - |  | 4.2 | 2.1 | 768 (max) | 119 (max) | 15.75 | 205 | 0.02
AMD EPYC 7601 (per socket) |  | - | - |  | 1.4 | 0.69 | 2000 (max) | 159 (max) | 15.75 | 180 | 0.008
Prace best practice guide – deep learning
https://en.wikipedia.org/wiki/Ampere_(microarchitecture)
CPUs have a lot of memory compared to GPUs
Notes: Add H100, add watt en perf per watt, add a10 inference

## Slide 16: Hardware overview
 | FP8 [TFLOPS] | INT8 [TOPS] | FP16 [TFLOPS] | Bloat16 [TFLOPS] | FP32 [TFLOPS] | FP64 [TFLOPS] | Memory [GB] | Memory Bandwidth [GB/s] | PCIe [GB/s] | Power draw [W] | FP16 TFLOP per Watt
AMD MI250 |  | 362.1 | 362.1 | 362.1 | 90.5 | 90.5 | 128 | 3276.8 | 31.51 | 560 | 0.64
AMD MI300x |  | 2615 | 1307 | 1307 | 654 | 163 | 192 | 5300 | 128 | 750 | 1.74
NVIDIA A100 |  | 624 | 312 | 312 | 156 | 19.5 | 40/80 | 1555-2039 | 64 | 400 | 0.78
NVIDIA H100 | 1979 | 1979 | 990 | 990 | 989 | 67 | 80/96 | 2000-3900 | 128 | 700 | 1.32
NVIDIA L40S (inference only) | 733 | 733 | 362 | 362 | 183 | 1.4 | 48 | 864 | 64 | 350 | 1.03
NVIDIA RTX 4090 (consumer) | 330 | 660 | 165 | 165 | 83 | 1.2 | 24 | 1000 | 64 | 400 | 0.41
Intel Xeon Scalable 8180 (per socket) |  | - | - |  | 4.2 | 2.1 | 768 (max) | 119 (max) | 15.75 | 205 | 0.02
AMD EPYC 7601 (per socket) |  | - | - |  | 1.4 | 0.69 | 2000 (max) | 159 (max) | 15.75 | 180 | 0.008
Prace best practice guide – deep learning
https://en.wikipedia.org/wiki/Ampere_(microarchitecture)
Memory bandwidth relative to FLOPS is approximately the same
Notes: Add H100, add watt en perf per watt, add a10 inference

## Slide 17: Hardware overview
 | FP8 [TFLOPS] | INT8 [TOPS] | FP16 [TFLOPS] | Bloat16 [TFLOPS] | FP32 [TFLOPS] | FP64 [TFLOPS] | Memory [GB] | Memory Bandwidth [GB/s] | PCIe [GB/s] | Power draw [W] | FP16 TFLOP per Watt
AMD MI250 |  | 362.1 | 362.1 | 362.1 | 90.5 | 90.5 | 128 | 3276.8 | 31.51 | 560 | 0.64
AMD MI300x |  | 2615 | 1307 | 1307 | 654 | 163 | 192 | 5300 | 128 | 750 | 1.74
NVIDIA A100 |  | 624 | 312 | 312 | 156 | 19.5 | 40/80 | 1555-2039 | 64 | 400 | 0.78
NVIDIA H100 | 1979 | 1979 | 990 | 990 | 989 | 67 | 80/96 | 2000-3900 | 128 | 700 | 1.32
NVIDIA L40S (inference only) | 733 | 733 | 362 | 362 | 183 | 1.4 | 48 | 864 | 64 | 350 | 1.03
NVIDIA RTX 4090 (consumer) | 330 | 660 | 165 | 165 | 83 | 1.2 | 24 | 1000 | 64 | 400 | 0.41
Intel Xeon Scalable 8180 (per socket) |  | - | - |  | 4.2 | 2.1 | 768 (max) | 119 (max) | 15.75 | 205 | 0.02
AMD EPYC 7601 (per socket) |  | - | - |  | 1.4 | 0.69 | 2000 (max) | 159 (max) | 15.75 | 180 | 0.008
Prace best practice guide – deep learning
https://en.wikipedia.org/wiki/Ampere_(microarchitecture)
GPU price is often irrelevant, but the performance per Watt is.
Notes: Add H100, add watt en perf per watt, add a10 inference

## Slide 18: Nvidia Volta (e.g. V100, TitanRTX)
Features
INT8 & FP16 support
(Volta) Tensor cores: fused multiply-add units that support mixed precision (multiply in FP16, add in FP32). High performance: 120 TFLOPS (for the time).
High bandwidth memory, 2nd generation (HBM2) (vs. DDR)
Generally, you are responsible for specifying a reduced precision: DL frameworks don’t do this automatically since it may impact your networks accuracy, convergence, etc

## Slide 19: Nvidia Ampere GPUs (e.g. A100)
Features (see also https://servicedesk.surf.nl/wiki/display/WIKI/Deep+Learning+on+A100+GPUs )
Tensor Cores support more datatypes (FP64, TF32, FP16, BF16, Int8, Int4, Binary)
TensorFloat32 datatype:
Mixed precision uses FP16. Reduced range causes (potential) need for gradient scaling to prevent underflows

## Slide 20: Nvidia Ampere GPUs (e.g. A100)
Features (see also https://servicedesk.surf.nl/wiki/display/WIKI/Deep+Learning+on+A100+GPUs )
Tensor Cores support more datatypes (FP64, TF32, FP16, BF16, Int8, Int4, Binary)
TensorFloat32 datatype:
TF32 tries to combine best of both worlds: range of an FP32 (no gradient scaling needed), but with reduced precision (for speedup & less memory)

## Slide 21: Nvidia Ampere GPUs (e.g. A100)
Features (see also https://servicedesk.surf.nl/wiki/display/WIKI/Deep+Learning+on+A100+GPUs )
Tensor Cores support more datatypes (FP64, TF32, FP16, BF16, Int8, Int4, Binary)
TensorFloat32 datatype:
Automatically used unless
Environment variable NVIDIA_TF32_OVERRIDE=0 is set
torch.backends.cuda.matmul.allow_tf32 = False and torch.backends.cudnn.allow_tf32 = False are set

## Slide 22: Nvidia Ampere GPUs (e.g. A100)
Model | Precision | Throughput (img/s) | Speedup (compared to FP32) | Loss (1st iteration)
ResNet50 | FP32 | 455.9 | 1 | 7.457645893096924
ResNet50 | TF32 | 750.6 | 1.65 | 7.456507205963135
ResNet50 | FP16 (input) + FP32 (accumulator) | 1087.6 | 2.38 | 7.45703125
VGG19 | FP32 | 212.7 | 1 | 6.9077839851379395
VGG19 | TF32 | 550.3 | 2.59 | 6.907783508300781
VGG19 | FP16 (input) + FP32 (accumulator) | 1099.8 | 5.17 | 6.90625
DenseNet121 | FP32 | 391.9 | 1 | 6.96142053604126
DenseNet121 | TF32 | 591.5 | 1.51 | 6.961450576782227
DenseNet121 | FP16 (input) + FP32 (accumulator) | 876.2 | 2.24 | 6.9609375
Source: https://servicedesk.surf.nl/wiki/display/WIKI/Deep+Learning+on+A100+GPUs

## Slide 23: Nvidia Hopper GPUs (e.g. H100)
FP8 support
Transformer-specific optimizations

## Slide 24: And on CPU:
Notes: Add new cpus

## Slide 25: Second S: Software
PyTorch/TensorFlow vs Numpy
  PyTorch and TensorFlow have GPU support, Numpy does not
  Numpy on AVX2....brrrr
Support for CUDA (Nvidia), ROCm (AMD), <insert exotic hardware here>?
  E.g.: Intel SapphireRapids
  IPEX: https://github.com/intel/intel-extension-for-pytorch
  LUMI https://www.lumi-supercomputer.eu/
Support for lower precision
  BFloat16, Float16?

## Slide 26: Third S: Stack
Is my software compiled for my hardware
  Pip install … ?
  Module load PyTorch/1.12.0-foss-2022a-CUDA-11.7.0
Again: SapphireRapids? ROCm?
PyTorch is crazy: https://github.com/pytorch/pytorch/tree/main/third_party
  PyTorch has given up on generic software management
  Ptrblck: "

## Slide 27: Wait ... so what happens?
You call torch
  (Manual) Dispatching
  E.g. scatter_add_ -> Message passing in Graph-NNs
Torch (python) determines the most appropriate function to call
  Dispatching
Torch (C++/CU) calls the CPU/GPU kernel
  Dispatching
Low-level lib performs actual calculation
  Dispatching
PyTorch Dispatcher: http://blog.ezyang.com/2020/09/lets-talk-about-the-pytorch-dispatcher/
Your choices matter

## Slide 28: In practice: PyTorch + Snellius
We only have NVIDIA GPUs
  72x4=288 NVIDIA A100
  88x4=352 NVIDIA H100 (added recently)
Makes optimization a bit easier for you
You only need to spend a year sifting through documentation
  https://servicedesk.surf.nl/wiki/display/WIKI/Deep+Learning+on+A100+GPUs
  Or ask us... :)
  Every EINF/NWO small grants has a default of 4 consultancy hours

## Slide 29: Rapidfire: implementation details
How fast do you want to go?
What is your goal?
  Largest model possible?
  Best validation performance?
  Submit a paper to ISC '23?

## Slide 30: Rapidfire: implementation details
How fast do you want to go?
https://pytorch.org/docs/stable/notes/cuda.html
https://docs.nvidia.com/deeplearning/performance/dl-performance-memory-limited/index.html
https://docs.nvidia.com/deeplearning/performance/index.html
Duncan: "You can take any piece of code, spend 6 months optimizing it, and then write a paper about it"

## Slide 31: Rapidfire: implementation details

## Slide 32: Level 1: Shouldn't impact model convergence:

## Slide 33: Level 1: Shouldn't impact model convergence:
Avoid CPU-GPU sync
  Create tensors directly on the device
Don't aggregate tensors which still require grad, e.g.: losses.append(loss) (:o)
  instead, detach (loss.detach())

## Slide 34: Level 1: Shouldn't impact model convergence:
torch.backends.cuda.matmul.allow_tf32 = True
  The default in PyTorch (silently)
torch.set_float32_matmul_precision('high')
torch.backends.cudnn.benchmark = True
  Empirically benchmarks to find fastest method
Align bytes: multiples of 2, 8, 1024
  DNN libraries want nicely aligned memory
torch.channels_last
  Helps with memory alignment and reduces cache misses
Compile: PyTorch 2.0
  Big speedup, but sensitive to implementation

## Slide 35: Level 2: Danger zone
torch.backends.cuda.matmul.allow_fp16_reduced_precision_reduction = True
Lol:
torch.backends.cuda.matmul.allow_bf16_reduced_precision_reduction
Torch.set_float32_matmul_precision('medium')
Cast model and data to (B)Float16 before the forward pass
  We're not supposed to...but:

## Slide 36: Change your model
  Worst case scenario:

## Slide 38: Always
  Have a baseline
  Check convergence statistics

## Slide 39: Profile
  Get a grip on your model’s performance
  Profile
  Profile
  Profile
  Also important: profile

## Slide 40: More generally; listen to Duncan:
  Start small
  Have a goal
  Profile your code